City of Buchanan Septage Receiving Plan

WWTP Location:					Mailing Address:

502 River Street					302 North Redbud Trail

Buchanan, MI 49107					Buchanan, MI 49107

Bill Housand, Superintendent				Attn: Bill Housand

Hours of Operation: 8:00 am to 4:00 pm

Monday-Friday (Closed Weekends & Holidays)

Fees: $65 per 1000 gallons ($.065/gallon)

Septage Received: Domestic only (grease trap and commercial wastes are prohibited).

Required Prior To Discharging: All septage haulers must have an approved septage discharge application on file at the WWTP and complete a septage discharge delivery ticket before discharging each time.

Buchanan WWTP Operational Considerations

Design Flow: 1.33 MGD

Design BOD Loading: 1553 lbs./day

Average Daily Flow: .93 MGD

Average Flow Percentage of Design Flow: 70% per day

Average BOD Loading: 859 lbs./day

Average BOD Percentage of Design Loadings: 55% per day

Septage Receiving Description: Septage will be discharged from trucks through a gravity fed micro-screen unit. The micro-screen unit will be surrounded by a containment area with curbing and sloped floors to ensure any overflows are captured and drained into the influent channel. Discharged septage will then be added into the WWTP influent structure located in the SW corner of the facility. Use of the influent structure will ensure that the septage is metered, pretreated and flow equalized before being added to the reactor basins for treatment. Metering is performed by a parshall flume and an ultrasonic meter. Pretreatment is provided by the septage micro-screen, vortex grit separator and fine screen units located in the headworks building. Flow equalization is accomplished by mixing septage flows with plant influent flows in the 18,000-gallon headworks wet well before being pumped into the reactor basins.

Receiving Capacity: The City of Buchanan will accept up to 5% of the WWTP’s normal influent flow in septage volume each day, but reserves the right to refuse septage discharges based on operational considerations, at any time.

Service Area: Local Haulers from the Michigan counties of Berrien and Cass, will be allowed to discharge septage produced within a 25-mile radius of the WWTP (please reference the attached map). Haulers within this area will be able to discharge at the WWTP, the City of Buchanan makes no claim as a mandatory discharge site.